## Slide 1
Presented by:
Mert Sevim Kaan Özsoy Polat Öztürk
EE 463 Hardware Project DC Motor Driver Term Project

## Slide 2: Introduction & Project Objectives
Goal: Design a power electronic driver for a DC motor.
Adjustable DC output up to 180 V.
Input: 3‑phase AC Voltage.
Ripple frequency requirement: fripple > 1 kHz.
Simulations verify performance; components finalized.

## Slide 3: Topology Selection
Selected Topology: 3‑Phase Diode Rectifier + Buck.
Provides ~520 V stable DC bus, high reliability, low cost and easy to implement

## Slide 4: System Overview
3‑Phase rectifier converts 380 V AC → ~520 V DC.
Buck converter regulates 0–180 V DC.
Motor‑generator pair simulates load.
17 Ω load connected to generator output.

## Slide 6: Simulation: Rectifier Stage
Input 380 V_LL → peak diode voltage ~540 V.
Average output ~530 V DC.
Max diode current < 60 A.
Defines minimum ratings for rectifier hardware.

## Slide 7
Diode current at steady state
Diode current at maximum

## Slide 8
Output current

## Slide 9: Simulation: Buck Converter Stage
Switching frequency: 10 kHz.
L = 2.2 mH, C = 470 μF.
Voltage ripple < 1%.
Inductor: 0–20 A current, –170 to 370 V voltage swing.

## Slide 10
Voltage and Current Waveform of Inductor
Output Voltage Waveform of Buck Converter

## Slide 11: Control Strategy (Cascaded Loops)
Speed loop: speedref – speedmeasured → Ia,ref.
Current loop: Ia,ref – Ia → Va,ref.
PWM: Converts Va,ref to duty ratio at 10 kHz.
Field PI loop regulates field voltage to 180 V.
Soft start via ramped references.

## Slide 12: Component Selection (Power Stage)
Rectifier: VUO98‑16NO7 (1600 V / 105 A).
MOSFET: IXFH80N65X2 (650 V / 80 A).
Freewheeling diode: DSEI30‑06A (600 V / 30 A).
Ratings selected for safety margins and fast switching.
VUO98-16NO7 3-phase full bridge rectifier
IXFH80N65X2 N-Channel Power MOSFET
DSEI30-06A freewheeling diode

## Slide 13: Microcontroller & Sensing
MCU: TI LAUNCHXL‑F28379D for PWM and PI loops.
Voltage divider: 550 kΩ / 10 kΩ reduces 180 V to ~3.21 V.
Isolation amplifier: TI AMC1200.
Current sensing: ACS758lcb Hall‑effect sensor.

## Slide 14: Conclusion & Bonus Goals
Stable DC output with <1% ripple.
Simulation achieved 1.4 kW; target 1.6 kW.
Supports Tea Bonus and Single‑Supply Bonus.
Awaiting hardware feedback for final implementation.